## Slide 1: SYDE 575: Image Processing
Introduction
Read Textbook Chapters 1 & 2

## Slide 2: What is Digital Image Processing?
Definition: manipulation of digital image for enhancement, compression, transmission, information extraction or analysis
  “manipulation” involves denoising, enhancement, registration, color mapping, rescaling, feature point detection, illumination reduction, …
Digital image defined as a 2-d function: f(x,y)
‘x’ and ‘y’ are spatial (in-plane) coordinates
f(x,y) is the value (usually stored as discrete) at a spatial (x,y) location
With multiple images of the same scene, one can deduce 3-d geometry and pixels in the image could have 3-d coordinates e.g., f(x,y,z) where (x,y,z) represents spatial coordinates
A video is defined as a 3-d function: f(x,y,t) where ‘t’ represents time

## Slide 3: Computer Vision
Image Analysis: content extraction e.g., segmentation, shape description, boundary detection, mathematical morphology, texture feature extraction, motion estimation
Image Understanding: decision making based on content extraction; covered in SD372 and SD675
SD575 deals primarily with “Image Processing” and, later in the course, “Image Analysis”
Scene
Image Processing
Image Analysis
Image Understanding
Information
Notes: Can give an example wrt operational facial recognition.

## Slide 4: Why is image processing difficult?
Mapping from a 3-d world to a 2-d plane
Measured intensity is a function of many factors
Interpreting groups of pixels as interesting objects is easy for the human, but not for the computer
Loads of data to process!
Local windows versus global interpretation

## Slide 5: Early Image Processing
Newspapers needed to send pictures across the Atlantic Ocean quickly
Source: Gonzalez and Woods

## Slide 6: Early Image Processing
Capturing and transmitting images from space
Source: Gonzalez and Woods

## Slide 7: Electromagnetic Spectrum
Source: Gonzalez and Woods

## Slide 8: Machine Vision
Source: Gonzalez and Woods

## Slide 9: Thermal (Infrared) Imaging
http://www.nationalinfrared.com/image_browser.php

## Slide 10: Satellite VIR (Visible – Infrared) Imaging
Source: Gonzalez and Woods

## Slide 11: Satellite Radar Image of Sea Ice
Source: MDA

## Slide 12: X-Ray Imaging
Source: Gonzalez and Woods

## Slide 13: MRI Images
Source: Gonzalez and Woods

## Slide 14: Ultrasound Imaging
Source: Gonzalez and Woods

## Slide 15: Grey Scale vs Color
Grey scale: single band
Color: three images (red, green, blue) combined to create single image
Notes: Lena (Swedish) and Lenna (from Playboy to encourage correct pronunciation)

## Slide 16: Image Sensing
Source: Gonzalez and Woods

## Slide 17: Digital Image Acquisition Example
Source: Gonzalez and Woods

## Slide 18: Simple Image Formation Model
Image may be characterized by:
  Amount of source illumination incident on scene
  Amount of illumination reflected by objects in scene (r=0 for total absorption, and r=1 for total reflectance)

## Slide 19: Digital Image Representation
Source: Gonzalez and Woods
Notes: Fig 2.18

## Slide 20: Image Sampling and Quantization
Source: Gonzalez and Woods
Notes: Fig 2.16

## Slide 21: Example
Source: Gonzalez and Woods

## Slide 22: Spatial Resolution
Source: Gonzalez and Woods

## Slide 23: Gray-level Resolution
Source: Gonzalez and Woods

## Slide 24: Fundamental Steps
Source: Gonzalez and Woods

## Slide 25: Vision and Image Processing (VIP) Lab
UW Research Lab that conducts research in computer vision
Covers many applications: remote sensing, biomedical, video analytics, 3d reconstruction, etc.
Many connections to industry to conduct applied research
Directors: Profs. Clausi, Wong, and Fieguth
http://vip.uwaterloo.ca

## Slide 26: Graduate Studies
If you are interested in graduate studies, chat with faculty members in your field of interest
Make sure that you apply for scholarships
  NSERC/OGS applications due typically in October
We are always looking for a few new graduate students to conduct research in the VIP lab (start Spring or Fall terms)