Drag (D):

where	D	=	total drag

Dp 	=	pressure drag (dominant for flow over a road vehicle)

Df 	=	friction drag (dominant for flow over an airplane)

ps 	=	surface pressure

(w 	=	wall shear stress

dA	=	element surface area

Drag Coefficient (CD):

where A is the frontal area of the object

Note:	A ( dA

Pressure Coefficient (Cp):

Flow Over a Circular Cylinder:

(Note:	)

where	CD,p	=	pressure drag coefficient

a	=	cylinder radius

b	=	cylinder width (into the page)

dA	=	ad(b (ad( = arc length)

A	=	2ab (frontal area)

Solution Procedure:

Step 1: Find stream function ( or potential function ( by superposition of

elementary flows

or

Step 2: Find surface velocity V(,s at cylinder surface (r = a)

(Note: )

Step 3: Find surface pressure ps from Bernoulli equation

Step 4: Find pressure coefficient Cp or pressure drag coefficient CD,p

- where

Example:

The stream function for potential flow past a circular cylinder (radius = a and width = b) with circulation is given as:

The tangential velocity at the cylinder surface (r = a) is then calculated as:

- For , show that two stagnation points (at which ) appear on the surface at angles ( = 30( and 150(.

- Assume that on the front surface ( -90( ( ( ( 90( ), the velocity is given by the potential flow theory with  from which the surface pressure ps is computed by Bernoulli’s equation. On the rear surface ( 90( ( ( ( 270( ), the pressure is assumed equal to its value at ( = 210( to model the overall effect due to flow separation.

Compute the pressure drag coefficient CD,p, where

and

Note that

# Text boxes

U(

a

dA = ad((b

ps

d(

dD

K

(

U(

a

(



wdA

psdA