## Slide 1: ScreenCommander
Taking Control
Erick Engelke
Engineering Computing

## Slide 2: ScreenCommander
Ability to take over students’ monitors, get their attention away from Surfing
Ability to send live video to students screen with clarity better than projectors
Easily adjusted parameters to optimize for speed or quality (video content versus application screens)
Primarily a software solution, assuming adequate network bandwidth – very low cost

## Slide 3: Commercial Options
ClassNet was an expensive hardware solution which died years ago, had scaling, clarity and reliability issues
NetSupport School software solution could never scale to 120+ workstations, also no longer available

## Slide 4: ScreenCommander in Action
Takes Jpeg compressed image of the instructor’s screen approximately 10 times per second
This Jpeg compression consumes about one core of the CPU for 1080-ish screens.
Student workstations get updates from the server either 10 frames per second, 1fps, or 1/3 fps (every 3 seconds). The instructor can toggle between the various frame rates.
Instructor can adjust the quality from 100% to 1% to reduce network load, allowing increased the frame rate.
With a fast enough network, all the traffic gets delivered. If the network is slower, the frame rate drops.

## Slide 5: Network Delivery of Images
Currently using Unicast HTTP protocol, with clients querying frequently
Tested Multicast and Broadcast, neither offered sufficient reliability in the MM lab (2018), inevitably several computers would fail to receive some data, and the video suffered.
Two options for server with 120 clients:
  Use a server with spare CPU core and optional 10G or 2x1G Ethernets (i.e. one dedicated to video)
  Use a supplemental PC or Raspberry Pi 4 to fan out to the clients : SCMultiplier application

## Slide 6: SCMultiplier (Windows/Linux/Pi) Option
SCMultiplier is local software run on a dedicate Windows, Linux or Pi computer to assist with video delivery. A minimum 4 GB computer is recommended for this software.
The SCMuliplier computer acts as a traffic multiplier, offloading network CPU effort from the Instructor’s PC while efficiently fanning data out to clients. The instructor computer is only as loaded as if it had a single client.
The SCMultiplier computer communicates as a client to the server, and as a http server to the client workstations.
All client workstations listen only to the multiplier. This adds a small approximately 2 millisecond delay.
Using SCMultiplier with dedicated 1 Gbps Ethernet can serve 120 clients @ 80% quality, 10 frames per second of typical desktop screen images
For video content streaming the system can scale down the quality or add additional network cards or a 10GB card

## Slide 7: Instructor Control
From an instructor’s perspective, controlling the system is easy.
  Just click the ScreenCommander icon on the presenter computer when it is desirable to take over screens and broadcast video
  Close the ScreenCommander window to relinquish control back to the class
  Optionally, select one of three update speed (10 fps, 1 fps, 0.3 fps) or move the quality slider to reduce quality. These steps are not necessary for most applications.

## Slide 8: Limitations and Expectations
The system was designed for 120 workstations, but it can be scaled up to much larger distribution sizes, just requiring ample network resources and one or more SCMultiplier computers
The frame rate of 10 fps is largely due to the CPU effort of encoding Jpegs. There are GPU assisted algorithms which would improve the frame rate
The screen resolution of 1600x1000 was tested. 4K screen resolutions would require much more computing power and is not recommended.
The intended labs (Multimedia, Graphics lab) should be upgraded to have a few 10G ports, and local packets grown up to 9kB, which would improve performance significantly.